## Slide 1: Forecast the Short Term Electricity Load Demand for Panama Power System
Submitted by: Gary Sampson
Date: July 20, 2021

## Slide 2
Benefits of Short Term Electricity Load Forecasting:
Reduces operational planning uncertainty added by the intermittent production of renewable sources.
Minimizes the fossil fuels/hydro electricity production costs in the power grid.
Efficient power grid maintenance planning.
Project Objective
The main objective of this analysis is to forecast the short term electricity demand (MWh) for Panama power system using a Deep Learning Model.

## Slide 3
Exploratory Data Analysis
From mid-march 2020, there was a significant drop in load demand probably due to COVID-19 pandemic lockdown.
There were a few intermittent partial drop in load demand due to power supply and/or transmission problems.

## Slide 4
Statistical information for load demand data:
The load demand plot shows that there are several outlier values which may have been due to power system equipment failure. Replace the outliers with a new value of 500 MWh.
Standardisation of the dataset.

## Slide 5
Model | Hyperparameters | Validation Mean Absolute Error
Baseline LSTM | Learning rate(lr) = 1e-3 Window size(ws) = 96 Hidden layers(hl) = 2 | 0.3969
GRU | lr = 1e-4; ws = 96; hl = 2 | 0.3842
GRU | lr = 1e-4; ws = 96; hl = 3 | 0.3930
GRU with 1 convolutional layer | lr = 1e-4; ws = 96; hl = 2 | 0.4074
Wavenet with 9 Conv1D layers | lr = 1e-4; ws = 96 | 0.7071
GRU | lr = 1e-4; ws = 168; hl = 3 | 0.8551
GRU | lr = 1e-4; ws = 72; hl = 3 | 0.4619
GRU | lr = 1e-4; ws = 48; hl = 3 | 0.3581
GRU | lr = 1e-4; ws = 24; hl = 3 | 0.2740
Best model: GRU with hyperparameters; learning rate = 1e-4, dataset window size = 24 and hidden layers = 3 with 300, 200 and 100 neurons respectively.

## Slide 6
Learning curves for best model:

## Slide 7
Load Demand Forecast Plots

## Slide 8
Test load demand Mean Absolute Error for best model: 17.95 MWh